## Slide 1: Class Problems
Module 4 – Climate Change Models

## Slide 2
Q1. Use the model presented earth and atmosphere energy balance equations to model the effect of an ice age. Suppose the combination of increased ice on the surface of the Earth and decreased CO2 in the atmosphere changes the parameters in the model as follows: αs = 0.15, t’a = 0.12, α’a = 0.23. All other parameters are unchanged. What are the new values of Ta and Ts?

## Slide 3
Q2A. Using a surface temperature value of 288 K, evaluate FBB(λ) at λmax, and also at λ = 5 μm (5 × 10–6 m) and 25 μm.
Q2B. Verify that the total flux across all wavelengths for a black body at 288 K sums approximately to the black-body radiation value given by Eq. (4-1):
Show this by summing values for all wavelengths by increment of 1 μm up to an appropriate value of wavelength such that flux is negligible.

## Slide 4
Q3. The planets Mars and Venus have albedo values of 0.15 and 0.75, and observed surface temperatures of approximately 220 K and approximately 700 K, respectively. The average distance of Mars from the sun is 2.28 × 108 km, and the average distance of Venus is 1.08 × 108 km. What is the extent of the greenhouse effect for these two planets, measured in degrees kelvin?

## Slide 5
Q4. Determine Ta and Ts due to the change t’a from 0.06 to 0.02. All other parameters remain the same the base case scenario. Also determine all energy streams in the 1-D climate change model.