## Slide 1: Module 1
Class Problems

## Slide 2
Q1. Determine the volumetric flow rate of natural gas, in ft3 /min, to heat water from 70°F to 120°F at volumetric flow rate of 20 gpm. Assume average heating values provided in slides for natural gas and a density of 8.3 lbm/gallon for water. Estimate yearly CO2 emission assuming an AFUE of 80% for the combustion process.

## Slide 3
Q2. To keep a single family home warm and cozy during a cold winter day, you may need to generate as much as 50,000 Btu/hr. Determine daily fuel consumption for an oil or gas furnace assuming a combustion process efficiency of 90%.

## Slide 4
 | Eligible | Enrolled
Primary | 2,500,000 | 2,375,000
Secondary | 2,100,000 | 1,953,000
University | 1,470,000 | 558,600
Q3. A country has a population of 31 million and consumes on average 12.09 exajoule (EJ) of energy per year. The life expectancy of the country is 63 years, and the country’s GDP is $0.4278 trillion dollars. The adult literacy rate is 75%. The eligible and actual student enrollments for primary, secondary, and college/university levels of education are given in the table below:
a. Calculate the HDI for this country.
b. How does this country’s HDI to energy intensity ratio compare to that of the countries in the scatter charts in the chapter? Is it above, below, or on a par with these other countries?

## Slide 5
Q4. Determine the yearly coal consumption of a 350 MW power plant, assuming a thermal cycle efficiency of 38% (thermal to mechanical conversion efficiency), overall combustion efficiency of 80%, and generator efficiency of 90%. Plant has a yearly availability of 90%. Estimate CO2 emission of the plant in metric tons.

## Slide 6
Q5. As energy costs continue to rise, power efficiency is increasingly important. Acme Chemical is evaluating two different electric motors to drive a mixing motor and needs to perform a present economy study. The motor will produce 75 hp and will be operated eight hours per day, 365 days for one year (maintenance does not affect average 8 hr/day operation), after which time the motor will have no value. Select the most economical motor. Assume Acme’s electric power costs $0.16 per kWh.
 | Motor A | Motor B
Purchase price | $3,200 | $5,900
Average lifetime maintenance cost | $250 | $450
Efficiency | 75% | 85%

## Slide 7
Q6. Estimate the annual electricity consumption of a 5 ton AC unit with SEER of 16 running approximately 1200 hrs/year.